KẾT QUẢ KHẢO SÁT CHẤT LƯỢNG NƯỚC BỂ BƠI

TẠI HẢI PHÒNG, NĂM 2013 - 2014

Đỗ Mạnh Cường*

# TÓM TẮT

Tiến hành khảo sát chất lượng nước bể bơi tại Hải phòng trong 2 năm (2013-2014), kết quả cho thấy:

# - Số mẫu có pH đạt tiêu chuẩn cho phép từ 6 - 8,5 chiếm tỷ lệ 81,18%.

# - 100% mẫu nước bể bơi có chỉ tiêu độ đục, sắt, NO2-, NO3-, NH4+, tổng chất rắn hòa tan và các kim loại nặng như Asen, Chì, Đồng, Kẽm đạt tiêu chuẩn cho phép. Các chỉ tiêu: độ cứng 90.57%, NaCl 84.91%.

- Tỷ lệ mẫu đạt tiêu chuẩn về chỉ tiêu clo dư 54.71% và DO là 22.64%.

- Năm 2014 có tỷ lệ mẫu đạt tiêu chuẩn cho phép cao hơn năm 2013 cả về chỉ tiêu hóa học và vi sinh vật.

SUMMARY

RESULTS OF SURVEY ON WATER

QUALITY AT SWIMMING POOLS

IN HAI PHONG IN 2013 – 2014

Results of the survey on water quality at swimming pools in Hai Phong in two years (2013-2014) showed that:

# - The percentage of water samples meeting pH standard from 6 – 8.5 is 81.18%.

# - 100% of the water samples meet the relevant standards for turbidity, Fe, NO2-, NO3-,NH4+, total dissolved solid and heavy metals, including Arsenic, Maganese, Cu, and Zinc. 90.57% of the samples meet the indicator of hardness, 84.91% meet the NaCl indicator.

- 54.71% of the water samples meet the requirement of residual Chlorine, 22.64% of the samples meet the requirements of DO.

- In 2014, number of samples meeting standards for chemical and organic indicators is higher than those in 2013.